Static analysis of beam structures using refined 1D beam model
    Presented by : Arun Prakash Ganapathy (63876) Supervised by: Mr. Jeffy Sabu Abraham

---
Hier steht die Kapitelüberschrift
INTRODUCTION
- Beam structures are widely used in many engineering applications such as aircraft wings, helicopter blades, concrete beams in constructions etc.,
- Classical 1-D models for beams made of isotropic materials are based on Euler-Bernoulli beam and Timoshenko theories.
- 1D refined models use polynomial expansions (like Taylor,Lagrange polynomials etc.,) to approximate the displacement values across the cross section of the beam.
- FE discretization on the axis of the beam element (1D) and an expansion across the cross section (2D) which gives the displacement field.
- The displacement function can be written in the compact form as
  u = Ni(y) Fτ(x,z)uτi τ = 1,2,3...M i = 1,2...

---
Aim of the project
Cantilever beam
Elliptical cross-section
Square cross-section
Isotropic material of Young’s modulus E and Poisson's ratio ν, has been considered for the analysis of the above beam structures
The aim of this project is to write an FE solver to compute displacements, strains and stresses across the cross-section of the beam using refined 1D beam models and to compare with analytical solutions and FEM software models (NASTRAN)

---
Theory behind refined beam models
- The basic governing equation behind the analysis of static response by principle of virtual displacement is given by the eqn δLint = δLext
- In case of refined 1D models the virtual variation of the internal work is given by δLint = ∫δεT σ dv = δusj kτsij uτ, where kτsij is the index notation of the stiffness matrix
- And the external work is given by δLext = P δuT = Fτ PδuτT, where Fτ is the expansion function across the cross section
- The expansion function considered here are the lagrange polynomial expansion of the displacement variables across the cross-section of the beam
- The unknown variables are only displacements of the nodes. No rotation or higher-order variables are used to describe the displacement field

---
Lagrange expansion polynomial:
1D shape functions along beam axis (Y)
2D Lagrange expansion (L4) across the cross-section
Fundamental nuclei for creating stiffness matrix kτsij :
Source: Finite element analysis of structure through unified formulation (Book by E.Carrera et al)
F_{\tau} = \frac{1}{4} (1 + \alpha \alpha_{\tau} ) (1 + \beta \beta_{\tau} ) \; \; \tau = 1, 2, 3, 4

---
Example:
      For a linear beam element (B2) with Lagrange expansion (L4) and for T, s = 2, i = 1 and j = 2
Source: Finite element analysis of structure through unified formulation (Book by E.Carrera et al)
Structure of the stiffness matrix kτsij:
Nodal stiffness matrix
Element stiffness matrix
Global stiffness matrix
$ k^{2122}_{xx} = C_{22} \;\int_{-a}^{+a} \int_{-b}^{+b} F_{2,x} F_{2,x} dx dz\; \int_{0}^{L} N_1 N_2 dy\; + \; C_{66} \int_{-a}^{+a} \int_{-b}^{+b} F_{2,z} F_{2,z} dx dz \; \int_{0}^{L} N_1 N_2 dy \;+$ \indent $\; C_{44} \int_{-a}^{+a} \int_{-b}^{+b} F_2 F_2 dx dz\; \int_{0}^{L} N_{1,y} N_{2,y} dy $
$ k^{2122}_{xx} = \frac{1}{18} \frac{b L}{a} C_{22} \; + \; \frac{1}{18} \frac{a L}{b} C_{66} \; - \; \frac{4}{9} \frac{b a}{L} C_{44} $

---
Load vector:
The virtual variation of the external work due to load P, in refined beam model is given by
For a cantilever beam loaded by a downward force P at the central point of the tip cross-section
Post-processing (Displacement, stresses and strains)
To find strains, partial derivatives are required which can be calculated utilizing shape and expansion functions
\delta L_{ext} = F_{\tau}N_{i}P\delta u^{T}_{\tau i}
\delta L_{ext} = P F_{1} u_{z_{11}} + P F_{2} u_{z_{12}} + P F_{3} u_{z_{13}} + P F_{4} u_{z_{14}}
\delta L_{ext} = \frac{P}{4} u_{z_{11}} + \frac{P}{4} u_{z_{12}} + \frac{P}{4} u_{z_{13}} + \frac{P}{4} u_{z_{14}}
u_{x}(x_{p},y_{p},z_{p}) = N_{i}(y_{p}) F_{\tau}(x_{p},z_{p})u_{x_{\tau i}}
u_{y}(x_{p},y_{p},z_{p}) = N_{i}(y_{p}) F_{\tau}(x_{p},z_{p})u_{y_{\tau i}}
u_{z}(x_{p},y_{p},z_{p}) = N_{i}(y_{p}) F_{\tau}(x_{p},z_{p})u_{z_{\tau i}}
u,_{y} = (F_{\tau} N_{i} u_{\tau i}),_{y} = F_{\tau} N_{i,y} u_{\tau i}

---
Results and Discussion
 (Square cross-section)
Verification
Stiffness matrix test - The 15*3 component of the element stiffness matrix computed using the implemented model is 1.522*1010 and the analytical solution is 1.544*1010.
Tension test - For a tension load of 50N the model predicted a deformation of 2.96*10-8m and the exact solution is 3.3*10-8m
Maximum vertical displacement (uz) :
The analytical solution for maximum vertical displacement is given by
u_{z} = \frac{P_{u_{z}} L^{3}}{3 E I}

---
Maximum axial strains and stresses (εyy, σyy)
The analytical solution for maximum strain and stress is given by and
respectively
Stress, strain distribution at the fixed end cross-section
\epsilon_{yy} = \frac{P_{u_{z}} L h}{2 E I}
\sigma_{yy} = \frac{P_{u_{z}} L h}{2 I}

---
Y displacement of the tip cross-section
Element type	uy*107 [m]
Nastran sol.	9.99
B2	6.74
B3	9.31
B4	6.74
Tilting of the end cross-section
Elliptical cross-section
Maximum vertical displacement (uz)
Element type	uz*107 [m]
Nastran sol.	-7.08
B2	-5.84
B3	-8.01
B4	-5.84
Bending of the beam

---
Y displacement of the tip cross-section
Element type	uy*107 [m]
Nastran sol.	1.05
B2	0.84
B3	1.15
B4	0.84
Tilting of the end cross-section
Stress, strain distribution at the fixed end cross-section